The Dump Divergence Bug
To make a dump from which a simulation can be resumed the entire state must be saved, i.e. all WELL states, the IDGen state, the state of the agent controller m_pAgentController (including the states of its L2Lists), as well as the array of previous deaths, m_pPrevD (for recycleDeadSpaceNew().

Experimental dumps and restores showed that the resumed simulation started to diverge after a certain number of steps (sometimes several hundred). Intense debugging showed that before the divergence all states of the resumed simulation were equal to the states of the original simulation.
However the first divergence was caused by an agent traveling to Australia in the original simulation but not in the resumed one.

The problem was in the Navigate module: when the environment changed, the existing seaways were not removed, which meant that the number of seaways increased. Therefore, agents in the original simulation had more opportunities to reach Australia than in the resumed simulation with its fewer seaways.

After adding a cleanup() method to Navigate that was called in recalculate() before every update, the problem was solved - resumed simulations ran identically to the original ones.